MAYDAY CALL 	                                    TRANSPONDER CODES

MAYDAY, MAYDAY, MAYDAY

NAME OF STATION BEING CALLED

G-BYTK

JABIRU SPL

NATURE OF EMERGENCY

INTENTION

POSITION

ALTITUDE

HEADING

P.O.B

V – SPEEDS

| STALL CLEAN | 47 KIAS |
| --- | --- |
| STALL FULL FLAPS | 43 KIAS |
| BEST GLIDE | 72 KIAS |
| ENGINE FALIURE AFTER TAKE OFF | 60-65 KIAS |
| APPROACH SPEED NORMAL (WITH FULL FLAPS) | 57 KIAS |
| APPROACH SPEED – SHORT FIELD | 55 KIAS |
| APPROACH SPEED (CLEAN) | 70 KIAS |
| BEST MANOUVERING | 91 KIAS |

EMERGENCY CHECKLIST

ENGINE FALIURE DURING FLIGHT

| 1 | Airspeed | 72 KIAS |
| --- | --- | --- |
| 2 | Landing Site | CHOOSE |
| 3 | Landing Site | HEAD TOWARDS |
| 4 | Carb Heat | ON |
| 5 | Fuel Shutoff Valve | ON |
| 6 | Fuel Pump | ON |
| 7 | Magnetos | BOTH ON |

ENGINE MAY RESTART IF PROPELLER IS STILL WINDMILLING.

EMERGENCY AIRSTART

IMPORTANT: DO NOT CRANK STARTER WHILE PROPELLER IS ROTATING.

| 1 | Magnetos | OFF |
| --- | --- | --- |
| 2 | INCREASE ANGLE OF ATTACK UNTIL PROP STOPS ROTATING | UP TO AND INCLUDING A STALL |
| 3 | Establish Glide | 72 KIAS |
| 4 | Fuel Shutoff Valve & Fuel Pump | ON |
| 5 | Master | ON |
| 6 | Magnetos | OPERATE STARTER |
| 7 | Throttle | OPEN |

REPEAT AS NECESSARY ENSURING PROPELLER HAS STOPPED ROTATION BEFORE EACH ATTEMPT.

# Text boxes

| 7000 | CONSPICUITY |
| --- | --- |
| 7500 | HIJACK |
| 7600 | RADIO FALIURE |
| 7700 | EMERGENCY |

EMERGENCY RADIO FREQUENCY

121.5